## Slide 1: 2015 Electrical Training
Presented by:
Richard Hathcoat
&
Alexander Millan

## Slide 2: Agenda
Electricity 101: Current vs. Voltage
Understanding Cable Sizes
FIRST Rules for wiring
Wiring best practices
Wiring termination hands-on practice
Q & A

## Slide 3: Electricity 101: Current vs. Voltage
Comparisons
  Both related to electricity
  Voltage, Current, and Resistance – ohms law
    V=I/R
Differences
  Voltage hurts, but current kills!
  In circuits
    Series – currents are same, voltage is distributed
    Parallel – current is distributed, voltages are same

## Slide 4: Electricity 101: Current vs. Voltage (cont’d)
Relationship
  Current is the effect as Voltage is the cause
  No Current w/o Voltage
  Voltage can exist w/o Current

## Slide 5: Electricity 101: Current vs. Voltage (cont’d)
Current
What is Current?
  Flow of electric charge across an element
  Symbol = I
Scenario
  Connect a tube to a tank. Now place an obstruction (Resistance) in middle of tube. If the tube is small, then the water flow would be less (less current flow). If the tube is large, then the water flow would be greater (more current flow).

## Slide 6: Electricity 101: Current vs. Voltage (cont’d)
Voltage
What is voltage
  Potential difference between 2 points
  Symbol = V
Types – AC, DC
Scenario
  2 water tanks. One half empty, one full. The difference of the water levels in the 2 tanks is similar to voltage difference.

## Slide 7: Electricity 101: Current vs. Voltage (cont’d)
Measuring Voltage Video using Multimeter
  https://www.youtube.com/watch?v=ZBbgiBU96mM
  10.28 to 17 mins
Measuring Current Video using Multimeter
  https://www.youtube.com/watch?v=GrgA9hReUHs
  7.05 to 11.18 mins

## Slide 8: Understanding Cable Sizes
The smaller the gauge #, the larger the wire
Different sizes are used for different applications
Each gauge size can carry a max amount of current
If bundle cables then current rating decreases

## Slide 9: Understanding Cable Sizes (cont’d)
“Thin wall” Cable
  Thin layer of insulation
  Higher grade
  Lighter/denser
  More resistant to impact damage
  Used in aviation
“Tinned” Cable
  Looks silver when insulation stripped
  Does not corrode as easily
  Use heat shrink at end to help prevent corrosion
# of strands in cable
  More strands = more flexible
  Increased cost

## Slide 10: FIRST Rules for wiring
FIRST Rules recommend:
Organized wiring
Tight connections

## Slide 11: FIRST Rules for wiring (cont’d)
Common Wiring Problems / Solutions
  1) Problem: Plug on Tetrix battery not reliable
  Solution: replace with quick-disconnect plug
  2) Problem: Crimp-on connectors – never use on solid core wire
  Solution: Cut tinned section / replace with new blade connector
  3) Problem: Screw terminals cause loose connections
  Solution: Use Ferrules or End Sleeves to avoid wire strays and a better connection

## Slide 12: FIRST Rules for wiring (cont’d)
Proper Wiring Management
  Keep wiring stationary
  Protect Wiring – use wire loom
  Cut cables to correct length

## Slide 13: Wiring best practices
Wiring Rules
  P.S. & Motor – use shielded twisted pairs
  Keep away from signal-carrying wires
  <5 feet – use 20 gauge for Motor wiring
  >5 feet – use 18 gauge or larger

## Slide 14: Wiring termination hands-on practice
Termination Types
Solder Type
  Strong/solid connection
  More reliable
Crimp Type
  Quick / simple
  Use proper size connector
  Use proper crimp tool
Good solder job
Bad solder job

## Slide 15: Wiring termination hands-on practice (cont’d)
Hands-on Practice
  How to attach 2+ wires together
  Find which size termination to use
  How to cut off wire insulation
  Knowledge check of the basic principles of wiring

## Slide 16: Contact Information
Have questions or need help in the future!
  Email me at rfhathc3@bechtel.com

## Slide 17
QUESTIONS ???